## Slide 1: KARPAGA VINAYAGA COLLEGE OF ENGINEERING AND TECHNOLOGY DEPARTMENT OF BIOMEDICAL ENGINEERING DESIGN AND DEVELOPMENT OF SMART SPOON FOR PATIENTS WITH PARKINSON’S DISEASE USING ARDUINO NANO
TEAM MEMBERS :
ARAVIND.S (421219121003),
PRAVIN MOTHI.M (421219121024),
PREETHI.J (421219121025),
RAJALAKSHMI.S.R (421219121026).
GUIDED BY:
Mrs.K.S.ABBIRAME,
ASSISTANT PROFESSOR,
DEPARTMENT OF BIOMEDICAL ENGINEERING.

## Slide 2: INTRODUCTION :
The technology for assisting people who are functionally challenged has improved over the recent decades. With today’s technology, people with Parkinson’s disease can, with a device on their wrist, be able to draw Pictures
A prototype of a stabilizing spoon was constructed to work under real circumstances and intended to be a complement for people who are in need of assistance during their eating process.
There are commercially available feeders that are useful for people who have controlled movements of the head and neck and can take food off of a feeding utensil that is brought close to the mouth.

## Slide 3
OBJECTIVES:
To setup the design and Arduino and Inertial measurement unit.
To fit the servo motors with the Arduino and Inertial measurement unit.
To program codes for the inertial measurement unit with Arduino.
To make the 3D design for the smart spoon.
To assemble the Arduino and inertial measurement unit with the with the 3D design.
AIM:
To design and development of smart spoon for patients with Parkinson’s disease using Arduino Nano.

## Slide 4
TITLE | AUTHOR | YEAR | PUBLICTION | INFERENCE
Adjustable spoon for Parkinson’s suffer | Ayushi Verma, Mahendra Shing meena | 2019 | International journal for Rechard in applied sciences and technology. (Amity university, Haryana) | Using this spoon the person with PD can eat without shaking , Spoon will always remaining facing upwards so that food does not fall down from the spoon.
Stabilizing spoon | Johan Danmo | 2021 | ITM | The spoon doesn’t react fast enough to be useful for the people with high frequency tremors. The reason to this that the motors are too slow to react for the motions. This stabilizing spoon can be utilized by people with impaired motor skills, though to certain extent.
REVIEW OF LITERATURE:

## Slide 5: MATERIALS OF METHADOLOGY :
DESIGN AND DEVELOPMENT OF SMART SPOON FOR PATIENTS WITH PARKINSON’S DISEASE
DESIGNING OF 3D SPOON HADEL
ARDUINO PROGRAMME CODING
ASSEMBLING THE 3D PARTS AND COMPONENTS TOGETHER
CALIBRATE THE SPOON FOR USE

## Slide 6
COMPONENTS | NECESSARY MACHINE | APPS
INERTIAL MEASUREMENT UNIT | 3D PRINTER | ARDUINO
SG90 MICRO-SERVO MOTOR | - | AUTODESK-FUSION 360
ARDUINO NANO R3 | - | -

## Slide 7: THEORY OF CONTENT : STABILIZING SPOON
A stabilizing spoon is a device which maintains a horizontal position of its front regardless of the motion it receives from the user at the rear end of the spoon.
For a theoretical demonstration of the spoon’s movement

## Slide 8: Microcontroller – Arduino Nano
It is a breadboard based on the microchip ATmega 328 and equipped with eight analog pins and 14 digital pins, of which six are PWM enabled The mini-USB port is used for programming but can also be used as a power source.
This means the board can be plugged into a computer and be programmed through Arduino’s own software.
Arduinos software is an Open-source code which is based on C/C++

## Slide 9: Servo motor
The dimension of the servo motor is 23.2 x 12.5 x 22.0 mm and weighs 9 grams as the name states.
The motor have 3 ins in total, one for the signals (PWM), one for the input voltage (Vcc).
operating voltage of about 4.8 V or 6 V and one for electrical ground (GND).

## Slide 10: IMU – MPU 6050
The MPU6050 combines a three-axis gyroscope and a three-axis accelerometer on the same board, along with an onboard Digital Motion Processor™(DMP™)
It can accurately track user motions. With the gyroscope and the accelerometer, which both are triple axis Micro Electrical Mechanical Systems (MEMS)
It can provide information of the boards angular position and acceleration.

## Slide 11: The Project ‘S Own Developed Code
The code that was developed by the project’s members has essentially three.
The part is bound to the declaration of each parameter used later in the code.
The second part is the initial setup, establishing communication between the microcontroller, servomotor and the IMU.
The third part is retrieving the value outputs from the IMU.
Which it later transforms into rotational commands for the servo motors through a complementary filter.

## Slide 12
Flowchart

## Slide 13: Hardware
All of the mounting parts and the casing were made out of PLA (hard plastic) constructed by an Ultimaker 2 3D printer.
The casing of Prototype i which is a hollow cylinder with details for mounting.

## Slide 14: Result & Discussion
In this section the performance of the spoon will be presented. The section will be divided into two parts where one is covering the results from the code that has been used from the similar stabilizing project and the other part is covering the results from the project’s own developed code.
The test rig used to gather numerical results of the reaction time where two Arduino Uno were connected with two IMU6050 separately to gather the data.

## Slide 15: References
[1] Franklin Parrales Bravo, Alberto A. Del Barrio Garcia, Mercedes Gallego de la Sacristana, Lydia Lopez Manzanares, Jose Vivancos and Jose Luis Ayala Rodrigo. Support system to improve reading activity in Published: 3 May 2017.
[2] Sreekanth Rudraraju and The Nguyen. Wearable Tremor Reduction Device (TRD) for human hands and arms. Published: 14 June 2018.
[3] Anupam Pathak, John A. Redmond, Michael Allen and Kelvin L. Chou. A non-invasive handheld assistive device accommodate essential tremor. Published: 27 Dec 2013.
[4] Erika Rovini, Carlo Maremmani and Filippo Cavallo. How wearable sensors can support Parkinson’s diagnosis and treatment: A systematic Review. 6 Oct 2017.
[5] Johan Abrahamsson and Johan Danmo. The stabilizing spoon. Published: Sweden 2017.

## Slide 16: THANK YOU